Pika Robot

Compass Module Calibration:

Pika Description:
Pika is a robotic rover that is built from the Pololu Zumo robot with several modifications allowing for obstruction detection and lighting.

Problem:
The compass module on the Pika robot is capable of measuring both acceleration and direction in three axis. The direction is determined by the magnetic pull on the compass module. Due to both normal variations and inaccuracies in the compass module as well as the magnetic pull of two motors and a servo on the Pika robot the compass module may not be accurate. This is compounded by the effect of the motors and servo on the compass while they are in operation. In order to accurately gauge the direction using the compass module we must run various tests and determine a reasonable range and method by which we can determine when we have pointed a certain direction in various conditions.

Test Procedures:
While under the operating environment of the test take 5000 readings from the compass module with the robot positioned in one of the four cardinal directions. After taking the 5000 readings they will be used to determine a reasonable max and min value that translates to the cardinal direction under that operating environment.

Operating Environments to Test:
Right motor forward 50, Left motor reverse 50
Right motor reverse 50, Left motor forward 50
Right motor forward 100, Left motor forward 100
Right motor reverse 100, Left motor reverse 100
Right motor forward 0, Left motor forward 0

Cardinal directions to test:
North
South
East
West

Constants:
Servo position of 90

Control:
Brunton Compass

Anomolies:
The bolts in the table I sit at cause the control compass to point to a false north.

Tests:

Sanity Check of the Test Sample Size
In order to determine an appropriate sample size for the test multiple tests were completed with Pika facing north with under the Right motor forward 50, Left motor reverse 50 operating environment. The following results were found:
200	400	1000	5000
	(130, 689)	(107, 678)	(115, 667)
	(120, 690)	(121, 673)	(116, 664)
	(98, 674)	(99,676)
	(117, 691)	(121,673)

A sample size of 5000 was decided on based on the reasonably small variations in mean calculated after multiple individual tests.

Right motor forward 50, Left motor reverse 50
Right motor reverse 50, Left motor forward 50
Right motor forward 100, Left motor forward 100
Right motor reverse 100, Left motor reverse 100
Right motor forward 0, Left motor forward 0